## Slide 1
Three-user Interference Channel with a Cognitive Transmitter: An Information Theoretic Perspective
Myung Gil Kang
Oct. 11, 2012
Wireless Communication Systems Laboratory (WCSL)
Korea Advanced Institute of Science and Technology (KAIST)
Notes: Good afternoon. Let me start my presentation. My name is Myung Gil Kang from KAIST Korea.
In this presentation, I will propose the Capacity of a Three-user Interference Channel with a Cognitive Transmitter in Strong Interference.

## Slide 2
Contents
Introduction
System Model
Capacity Region of the Strong Interference Channel
Interference Alignment with Rate Splitting
Conclusions
Notes: This is agenda of my presentation.
Firstly, I’ll introduce some related works. And I’ll explain about system model and the channel classification.
Then, the capacity region of the strong interference channel will be explained.
And the capacity region and channel conditions will be shown for Gaussian case.
Finally, I’ll conclude the presentation.

## Slide 3
Related works
  2 user interference channels
    [Han and Kobayashi, 1981]
    [Costa and Gamal, 1987]
    [Etkin et al., 2008]
    [Annapureddy and Veeravalli, 2009]
1st
Introduction
Notes: interference management is one of the most important issues in wireless communications system .
The conventional interference management schemes were orthogonalization of wireless resources such as freq/time/codes
This can be explained as cake cutting approach and each user obtains 1/K wireless resource in K –user IC.
For several years, interference alignment is proposed as new interference managing scheme.
The main concept of IA is to make the interfering signals aligned at each receiver.
In K-user IC, K/2 DoF is shown to be achieved.
And in K-user M×M interference channel KM/2 DoF is proved to be achieved.
All users can achieve the half of wireless resources.

## Slide 4
Related works
  K-user interference channels ()
    [Sridharan et al., 2008]
    [Cadambe and Jafar, 2008]
1st
Introduction
Notes: interference management is one of the most important issues in wireless communications system .
The conventional interference management schemes were orthogonalization of wireless resources such as freq/time/codes
This can be explained as cake cutting approach and each user obtains 1/K wireless resource in K –user IC.
For several years, interference alignment is proposed as new interference managing scheme.
The main concept of IA is to make the interfering signals aligned at each receiver.
In K-user IC, K/2 DoF is shown to be achieved.
And in K-user M×M interference channel KM/2 DoF is proved to be achieved.
All users can achieve the half of wireless resources.

## Slide 5
Related works
  2 user cognitive interference channels
    [Devroye et al., 2006]
    [Wu et al., 2007]
    [Maric et al., 2007]
    [Maric et al., 2008]
1st
Introduction
Notes: interference management is one of the most important issues in wireless communications system .
The conventional interference management schemes were orthogonalization of wireless resources such as freq/time/codes
This can be explained as cake cutting approach and each user obtains 1/K wireless resource in K –user IC.
For several years, interference alignment is proposed as new interference managing scheme.
The main concept of IA is to make the interfering signals aligned at each receiver.
In K-user IC, K/2 DoF is shown to be achieved.
And in K-user M×M interference channel KM/2 DoF is proved to be achieved.
All users can achieve the half of wireless resources.

## Slide 6
Related works
  2 user interference channels with a cognitive relay
    [Sahin and Erkip, 2007]
    [Sahin et al., 2009]
    [Rini et al., 2011]
1st
Introduction
Notes: interference management is one of the most important issues in wireless communications system .
The conventional interference management schemes were orthogonalization of wireless resources such as freq/time/codes
This can be explained as cake cutting approach and each user obtains 1/K wireless resource in K –user IC.
For several years, interference alignment is proposed as new interference managing scheme.
The main concept of IA is to make the interfering signals aligned at each receiver.
In K-user IC, K/2 DoF is shown to be achieved.
And in K-user M×M interference channel KM/2 DoF is proved to be achieved.
All users can achieve the half of wireless resources.

## Slide 7
Configuration
  S3: cognitive transmitter
  Sk: non-cognitive transmitter
  Memoryless and discrete channel given by
  If
  where denotes the capacity region of the 3-user IC with a cognitive Tx.
2nd
System Model

## Slide 8
Related works
  Capacity achievable schemes
 | Weak interference | Moderate interference | Strong interference
2 user IC | Treating interference as noise | Rate splitting (within one bit) | Jointly decoding
K-user IC | Unknown |  | Lattice coding (very strong)
2 user cognitive IC | Gel’fand-Pinsker coding | Unknown | Superposition coding with jointly decoding
2 user IC with a cognitive relay | Unknown |  | Superposition coding with jointly decoding
3 user IC with a cognitive transmitter | Unknown |  | 
3rd
Capacity Region of the Strong Interference Channel
Notes: interference management is one of the most important issues in wireless communications system .
The conventional interference management schemes were orthogonalization of wireless resources such as freq/time/codes
This can be explained as cake cutting approach and each user obtains 1/K wireless resource in K –user IC.
For several years, interference alignment is proposed as new interference managing scheme.
The main concept of IA is to make the interfering signals aligned at each receiver.
In K-user IC, K/2 DoF is shown to be achieved.
And in K-user M×M interference channel KM/2 DoF is proved to be achieved.
All users can achieve the half of wireless resources.

## Slide 9
Related works
  Capacity achievable schemes
 | Weak interference | Moderate interference | Strong interference
2 user IC | Treating interference as noise | Rate splitting (within one bit) | Jointly decoding
K-user IC | Unknown |  | Lattice coding (very strong)
2 user cognitive IC | Gel’fand-Pinsker coding | Unknown | Superposition coding with jointly decoding
2 user IC with a cognitive relay | Unknown |  | Superposition coding with jointly decoding
3 user IC with a cognitive transmitter | Unknown |  | Our work
3rd
Capacity Region of the Strong Interference Channel
Notes: interference management is one of the most important issues in wireless communications system .
The conventional interference management schemes were orthogonalization of wireless resources such as freq/time/codes
This can be explained as cake cutting approach and each user obtains 1/K wireless resource in K –user IC.
For several years, interference alignment is proposed as new interference managing scheme.
The main concept of IA is to make the interfering signals aligned at each receiver.
In K-user IC, K/2 DoF is shown to be achieved.
And in K-user M×M interference channel KM/2 DoF is proved to be achieved.
All users can achieve the half of wireless resources.

## Slide 10
Sketch of the proof (Capacity region)
3rd
Capacity Region of the Strong Interference Channel
Inner Bound
Outer bound
Four channel conditions
Four channel conditions
=
Capacity region
with 8 channel conditions
Notes: Thus, we consider 3-dimensional complex sphere S0.
And S0 can be divided into two parts according to some direction c and the some thickness lambda.
And each part can be defined like this.

## Slide 11
Outer bound
  Theorem 3-1. For the interference channel conditions
  for all input distributions , the capacity region of a three-user interference channel with a cognitive transmitter has an outer bound
3rd
Capacity Region of the Strong Interference Channel
S3 → Dk: strong
Sk → Dl: strong
Notes: Thus, we consider 3-dimensional complex sphere S0.
And S0 can be divided into two parts according to some direction c and the some thickness lambda.
And each part can be defined like this.

## Slide 12
Outer bound
  for all input distributions .
3rd
Capacity Region of the Strong Interference Channel
Notes: Thus, we consider 3-dimensional complex sphere S0.
And S0 can be divided into two parts according to some direction c and the some thickness lambda.
And each part can be defined like this.

## Slide 13
Inner bound
  Theorem 3-2. If the cognitive transmitter adopts superposition coding and all decoders jointly decode all the messages, the achievable rate region is the set of all achievable rate triples such that
  for all input distribution .
3rd
Capacity Region of the Strong Interference Channel
Sk → D3: strong
Notes: Thus, we consider 3-dimensional complex sphere S0.
And S0 can be divided into two parts according to some direction c and the some thickness lambda.
And each part can be defined like this.

## Slide 14
Capacity region
  Theorem 3-3. For the interference channel condition which satisfies
  for all input distributions ,
3rd
Capacity Region of the Strong Interference Channel
Sk → D3: strong
S3 → Dk: strong
Sk → Dl: strong
Notes: Thus, we consider 3-dimensional complex sphere S0.
And S0 can be divided into two parts according to some direction c and the some thickness lambda.
And each part can be defined like this.

## Slide 15
Capacity region
  the capacity region of the three-user interference channel with a cognitive transmitter is determined by
  for all input distributions .
3rd
Capacity Region of the Strong Interference Channel
Notes: Thus, we consider 3-dimensional complex sphere S0.
And S0 can be divided into two parts according to some direction c and the some thickness lambda.
And each part can be defined like this.

## Slide 16
Rate splitting
  Split the message into two types
    Private message – Optimal in weak interference regime
    Common message – Optimal in strong interference regime
4th
Interference Alignment with Rate Splitting
Notes: Thus, we consider 3-dimensional complex sphere S0.
And S0 can be divided into two parts according to some direction c and the some thickness lambda.
And each part can be defined like this.

## Slide 17
Rate splitting
  Generalized DoF
4th
Interference Alignment with Rate Splitting
Weak
Strong
Notes: Thus, we consider 3-dimensional complex sphere S0.
And S0 can be divided into two parts according to some direction c and the some thickness lambda.
And each part can be defined like this.

## Slide 18
Interference alignment
  Half dimension for desired signal
  The other dimension for interference alignment
  1/2 DoF achievable for each user
4th
Interference Alignment with Rate Splitting
Notes: Thus, we consider 3-dimensional complex sphere S0.
And S0 can be divided into two parts according to some direction c and the some thickness lambda.
And each part can be defined like this.

## Slide 19
Interference alignment with rate splitting
  Key idea
    Dimension recycling
  Interference aligned effective channel
4th
Interference Alignment with Rate Splitting
Notes: Thus, we consider 3-dimensional complex sphere S0.
And S0 can be divided into two parts according to some direction c and the some thickness lambda.
And each part can be defined like this.

## Slide 20
  Encoding rule
4th
Interference Alignment with Rate Splitting
Notes: Thus, we consider 3-dimensional complex sphere S0.
And S0 can be divided into two parts according to some direction c and the some thickness lambda.
And each part can be defined like this.

## Slide 21
Achievable rate region
  Theorem 4-1. The achievable rate region is determined by the convex hull of all non-negative rate triple (R1, R2, R3) such that
4th
Interference Alignment with Rate Splitting
Notes: Thus, we consider 3-dimensional complex sphere S0.
And S0 can be divided into two parts according to some direction c and the some thickness lambda.
And each part can be defined like this.

## Slide 22
4th
Interference Alignment with Rate Splitting
Notes: Thus, we consider 3-dimensional complex sphere S0.
And S0 can be divided into two parts according to some direction c and the some thickness lambda.
And each part can be defined like this.

## Slide 23
  for all input distribution
4th
Interference Alignment with Rate Splitting
Notes: Thus, we consider 3-dimensional complex sphere S0.
And S0 can be divided into two parts according to some direction c and the some thickness lambda.
And each part can be defined like this.

## Slide 24
Generalized DoF
  β = 0.5
4th
Interference Alignment with Rate Splitting
Notes: Thus, we consider 3-dimensional complex sphere S0.
And S0 can be divided into two parts according to some direction c and the some thickness lambda.
And each part can be defined like this.

## Slide 25
Generalized DoF
  β = 1
4th
Interference Alignment with Rate Splitting
Notes: Thus, we consider 3-dimensional complex sphere S0.
And S0 can be divided into two parts according to some direction c and the some thickness lambda.
And each part can be defined like this.

## Slide 26
Capacity region when all cross-channels are strong.
  Newly derived outer bounds are achieved by superposition coding and joint decoding.
Interference alignment with rate splitting
  Proposed scheme recycles the sacrificed dimension.
  GDoF becomes larger as γ increases.
5th
Conclusions

## Slide 27
Thank you for your attention